## Slide 1
MOOSE Introductory Workshop
Multi-physics Object-Oriented Simulation Environment
April 4, 2024
Joshua Hansel Computational Scientist Idaho National Laboratory

## Slide 2: Outline
Outline:
  Part 0: What is MOOSE?
  Part 1: How to install MOOSE
  Part 2: How to run a MOOSE input file
  Part 3: How to write a MOOSE input file
  Part 4: How to write MOOSE code (an introduction)
  Part 5: How to learn more MOOSE
  Open Q&A

## Slide 3: Part 0: What is MOOSE?

## Slide 4: The MOOSE Framework
Open-source, massively parallelizable, finite element framework written in C++, focusing on multiphysics coupling
Started in 2008, open-sourced and received R&D 100 in 2014
NQA-1 compliant
Some numbers:
  208+ contributors
  46,000+ commits
  5000+ unique visitors per month
  2000+ citations for MOOSE papers
  70M+ tests per week

## Slide 5: Overview of Capabilities
Continuous and Discontinuous Galerkin Finite Element Method (FEM), Finite Volume (FV)
Multiphysics, multiscale
Explicit or implicit time integration
Automatic differentiation (AD)
Unstructured mesh
Higher-order geometry
Mesh adaptivity (refinement and coarsening)
Massively parallel (MPI and threads)
User code agnostic of dimension, parallelism, shape functions, etc.
OS: Mac, Linux, or Windows (WSL)
Object-oriented, pluggable system

## Slide 6: Some INL Nuclear Applications
MOOSE
HPC Framework
Marmot
Mesoscale Materials
Grizzly
Structural Mechanics for
Component Aging
Bison
Nuclear Fuel Performance
Pronghorn
Porous Medium Flow
Sockeye
Heat pipe Simulation
RELAP-7
Multiscale Multiphysics
Systems Analysis
GRIFFIN
Reactor Multiphysics

## Slide 7: MOOSE Framework Ecosystem
MOOSE Framework
MOOSE Modules
MOOSE-Based Applications
MOOSE-Coupling Applications
MOOSE-Wrapped Applications
7
Notes: LMFR – liquid metal-cooled fast

## Slide 8: Part 1: How to install MOOSE

## Slide 9: Installing MOOSE
If on Windows, follow these instructions first: https://mooseframework.inl.gov/getting_started/installation/windows.html
Installation from source (recommended): https://mooseframework.inl.gov/getting_started/installation/conda.html cd ~/projects/moose/modules make –j 10
Installation of binary (can be done additionally or alternatively): https://mooseframework.inl.gov/getting_started/installation/moose_conda_binary.html
Examples for this workshop: cd ~/projects git clone git@github.com:joshuahansel/ans_workshop.git cd ~/projects/moose mkdir ans_workshop cp ../ans_workshop/* ans_workshop

## Slide 10: Part 2: How to run a MOOSE input file

## Slide 11: Executables
Executables for MOOSE only may be created/obtained via these instructions: https://mooseframework.inl.gov/getting_started/installation/index.html
Executables for existing MOOSE-based applications may be obtained by following their respective directions
Run moose -h to get a list of command-line options
Run serially: moose -i myinput.i
Run with 4 threads: moose -i myinput.i --n-threads=4
Run with 4 MPI processes: mpiexec -n 4 moose -i myinput.i
Exercise: Run heat_conduction.i all three ways, using the "-t" flag to produce a timing table

## Slide 12: Viewing Output
Output quantities, output frequency, and format are specified in the input file
Possible formats include:
  Exodus [*.e]: recommended for space-dependent variables
  CSV [*.csv]: recommended for scalar (0D) post-processed data
  XML [*xml]: recommended for vector post-processed data
  Others
Exercise: View the Exodus output file from heat_conduction.i in Paraview

## Slide 13: Part 3: How to write a MOOSE input file

## Slide 14: Finite Element Method Example
Consider the transient heat conduction equation:
Spatially discretize with Continuous Galerkin FEM:
  Choose a finite element type: first-order Lagrange
  Approximate the solution field:
  Multiply by the test function and integrate over the domain :
  Perform integration by parts:

## Slide 15: Finite Element Method Example
Split the integrals into integrals over elements.
Approximate the element integrals using numerical quadratures like Gauss quadrature.
Discretize the temporal derivative.
Now we have a system of algebraic equations (generally nonlinear):
Refer to as the nonlinear residual vector.
Choose a method to solve the nonlinear system, like Newton's method:

## Slide 16: Automatic Differentiation (AD)
Newton's method requires the calculation of the Jacobian matrix: i.e., it is the derivative of the nonlinear residual vector with respect to the solution vector
Hand-coded calculations of the Jacobian may be difficult to derive and error-prone
AD computes Jacobian contributions automatically by propagating derivatives via chain rule, so that developers do not need to implement Jacobians
Many MOOSE objects support AD. Some exist with two versions, one for AD and one for non-AD. The AD version gets the "AD" prefix

## Slide 17: Input File Structure
Block-based input file structure, with possible nesting: [MyBlock1] # stuff here [] [MyBlock2] [mysubblockA] # stuff here [] [mysubblockB] # stuff here [] []
Top-level block names correspond to certain systems or actions in MOOSE. Examples:
  [Mesh] for loading/generating a mesh
  [Outputs] for specifying output(s)
Sub-blocks usually correspond to MOOSE objects of that system. Users name these: [Kernels] [mydiffusion] type = Diffusion
Sometimes there are specifically-named sub-blocks in a block (sub-systems). Example: [Executioner] [TimeSteppers]

## Slide 18: Input File Structure
Blocks/sub-blocks have input parameters of various types:
  Floating-point numbers: param1 = 5.0
  Integers: param1 = 5
  Strings: param1 = "mystr"
  Lists of any of these: param1 = '2.0 45 4e-6'
Comments specified on any line with #: param1 = 5.0 # my comment
  They can be on their own line too
[GlobalParams] is a special block that substitutes its parameters anywhere where they apply, i.e., they are "global" parameters. You can locally override.

## Slide 19: Input File Features
Values can be defined at the top of the input file and substituted in multiple places: myval = 5 [Block1] [myobj1] type = ClassA param1 = ${myval} [] [myobj2] type = ClassB param2 = ${myval} [] []
You can evaluate math expressions: radius = 5 diameter = ${fparse 2 * radius} area = ${fparse pi * radius^2} For a list of operators: http://warp.povusers.org/FunctionParser/fparser.html#literals
You can convert units: param1 = ${units 1 in -> m} For a list of units: https://mooseframework.inl.gov/source/utils/Units.html

## Slide 20: Input File Features
You can use "include" statements in input files: !include otherinput.i This effectively substitutes that file's contents at this location. Parameters cannot be specified multiple times, i.e., there is no parameter-overriding in this way.
You can also supply multiple input files on the command-line: moose -i input1.i input2.i input3.i Input files to the right override those to the left.

## Slide 21: VSCode (Optional)
VSCode is an open-source text editor and integrated development environment
We recommend it because of support for MOOSE input files; the extension "MOOSE Language Support" provides:
  Syntax highlighting for MOOSE input files
  Autocompletion
  Class and parameter descriptions
Keyboard shortcut to bring up class/parameters boxes: Ctrl+Space
Additional setup if using pre-built MOOSE binary: conda env config vars set MOOSE_LANGUAGE_SERVER=$HOME/miniforge/envs/my-moose-env/moose/bin/moose
For more information: https://mooseframework.inl.gov/help/development/VSCode.html

## Slide 22: Common MOOSE Systems Overview
Mesh: Load/generate/modify a mesh
Variables: Define solution variables
AuxVariables: Define non-solution variables
AuxKernels: Define how to compute AuxVariables
Kernels: Define volumetric physics terms
BCs: Define boundary physics terms
Materials: Define "properties" at quadrature points
Functions: Define functions of x,y,z,t
Postprocessors: Define scalar quantities
VectorPostprocessors: Define vectors
Preconditioning: Define preconditioner matrix
Executioner: Define execution, like steady vs. transient, temporal discretization, and convergence
Outputs: Define output(s)

## Slide 23: Mesh System
MOOSE's mesh generator system can be used:
  To load an external mesh from a file (different formats possible), such as from an external mesh-generator like CUBIT.
  To generate meshes within MOOSE.
  To modify meshes.
Mesh generators are chained together to produce the final mesh.
To only generate the mesh without running the simulation, you can pass --mesh-only on the command line.

## Slide 24: Mesh Definitions
A node is a vertex of the mesh and has a global index, starting from 0.
An element is the volume between vertices and has an index, starting from 0.
A side is a face of an element and is defined by a local index, starting from 0.
A block is a set of elements, either the full mesh or a subset.
  A block has an ID (index, starting from 0) and may have a name too.
A boundary is either a side set or a node set.
  A side set is a set of (element, side) pairs.
  A node set is a set of nodes.
  Each type of set has an ID and may have a name too.
  Often side sets and node sets are mirrored with the same name.

## Slide 25: Meshing Exercise
Exercise: Build the mesh shown to the right.
  Hex apothem: 1 cm
  Length: 1 m
Strategy:
  Build 2D unit cells for fuel and reflector
  Assemble those into pattern
  Extrude
  Clean up
Fuel
Reflector

## Slide 26: Physics Problem Exercise
Problem specifications:
  Geometry/Material: (1 m X 0.2 m X 0.1 m) SS316 slab
  Left, right, front, back, bottom boundaries insulated
  Top boundary has convection: with W/(m2-K), K
  Uniform, volumetric source of 1 kW
Objectives:
  Find the steady-state solution from the heat conduction equation.
  Verify conservation of energy.
  Get the max/min temperatures.
  Get the steady temperature distribution along the top.

## Slide 27: Variables and AuxVariables
Variables are in the solution vector
  May be field variables (PDEs) or scalar variables (ODEs)
  Field variables have a finite element family and order
AuxVariables are not in the solution vector
  Explicitly calculated at nodes via corresponding object:
    AuxKernels for field variables
    AuxScalarKernels for scalar variables
  Used mostly for output purposes
  Main vehicle for transfers to other apps
  No AD support, so not recommended for internal calculations
    Prefer material properties instead
Output treats Variables and AuxVariables equally
ICs define initial conditions or initial guess for each variable

## Slide 28: Residual Systems
Various systems add contributions to the residual vector :
  Kernels implement volumetric terms
  DGKernels implement terms on internal sides
  BCs implement terms external sides
    IntegratedBC is the base class for side integral terms
    NodalBC is the base class for nodal terms, like DirichletBC
  ScalarKernels implement terms for ODEs
  Others
Each residual object is associated to a solution variable, which determines which entry of the residual vector to contribute to

## Slide 29: Materials System
Each Material creates one or more material properties.
Material properties are quantities that are computed at each quadrature point.
Various systems may then use these material properties.
A material property may be AD or non-AD, and consuming objects expect one or the other.
  MaterialADConverter can convert between the two types (note non-AD to AD must be used with care).
Similar system: FunctorMaterials
  Creates one or more functor material properties.
  Computed "on-the-fly"
  Unlike regular material properties, are functors.

## Slide 30: Executioner System
The executioner determines which kind of problem to solve, like:
  Steady
  Transient
  Eigenvalue
  Others
This system has subsystems like:
  TimeIntegrator: For Transient: the time integration scheme to use
  TimeStepper: For Transient: how to compute time step size
  Quadrature: Rule to use for numerical integrations on elements/sides
Also specifies solve parameters (next slide)

## Slide 31: Solve Parameters
Solve type specified in Executioner block:
  NEWTON
  PJFNK
  LINEAR
Solve parameters like convergence tolerances
Steady-state detection for Transient
PETSc command-line flags can be supplied
A Preconditioning block can be specified to customize the preconditioning

## Slide 32: Functions System
Functions define functions
  Occasionally there are exceptions that allow for other variables
These can be used by a objects in a variety of systems

## Slide 33: Postprocessors and VectorPostprocessors Systems
Postprocessors compute a single, scalar value
  Typically used for post-processing
  Can be output to CSV files
  Examples:
    Sample a quantity at a particular point
    Find the max/min/integral/average of a quantity over a block/boundary
VectorPostprocessors compute one or multiple vectors of values
  Can be output to CSV and XML files
  Examples:
    Sample a quantity along a boundary at each node

## Slide 34: Outputs System
Outputs specify output, whether to the console or to a file.
Common classes:
  Console
  CSV
  Exodus
  XMLOutput

## Slide 35: UserObjects System
Flexible system that allows users to define their own operations to perform
Other objects can call user-defined interfaces on these UserObjects
Types:
  GeneralUserObject: does not operate on a mesh entity
  ElementUserObject: operates on each element
  SideUserObject: operates on each side
Postprocessors and VectorPostprocessors are just UserObjects that are responsible for producing certain values

## Slide 36: Part 4: How to write MOOSE code

## Slide 37: Prerequisites
Knowledge of C++
  Object-Oriented Programming (OOP)
  Classes, inheritance
  Templates (advanced; may not necessarily need)
Knowledge of git
  Need to fork MOOSE and/or the "stork" to initiate your repo(s).
  Need to add, commit, push, and fetch/pull your changes to repos.
  For new applications, MOOSE will be a submodule.
  Collaborative workflows also require knowledge of rebase and merge.

## Slide 38: Getting Started
Decide if you want to make a new application or just work with MOOSE.
Reasons to make your own application:
  Privacy: protect intellectual property or sensitive material
  Freedom of software development; don't need to follow NQA-1 for example.
Reasons to contribute to MOOSE:
  Others can take advantage of your work (and cite it).
  May be more convenient than making your own application.
If making your own application:
  You must run the "stork" script to initialize your new repo: https://mooseframework.inl.gov/getting_started/new_users.html
If not making your own application, you should simply fork MOOSE: https://mooseframework.inl.gov/framework/contributing.html

## Slide 39: Code Example
Consider the Diffusion kernel. The base class is Kernel.
Header file located at framework/include/kernels/Diffusion.h
Source file located at framework/src/kernels/Diffusion.C
We must override the method Real computeQpResidual() and optionally can override Real computeQpJacobian().
  These correspond to the residual and Jacobian matrix evaluations at a quadrature point.
Exercise: View the above files and discuss each line.

## Slide 40: Source Code Examples
Kernel: Diffusion
BC: NeumannBC
Postprocessor: ElementIntegralPostprocessor
AuxKernel: FunctionAux
IC: RandomIC
Material: GenericFunctionMaterial
FunctorMaterial: GenericFunctorMaterial
Function: LinearCombinationFunction
VectorPostprocessor: SideValueSampler

## Slide 41: Part 5: How to learn more MOOSE

## Slide 42: MOOSE Website
Located at https://mooseframework.inl.gov/index.html
Highlights:
  Installation instructions: https://mooseframework.inl.gov/getting_started/installation/index.html
  Examples and tutorials: https://mooseframework.inl.gov/getting_started/examples_and_tutorials/index.html
  Upcoming trainings and recordings of past trainings: https://mooseframework.inl.gov/training/index.html
  Help forum: https://github.com/idaholab/moose/discussions
  Documentation: https://mooseframework.inl.gov/syntax/index.html

## Slide 43: Additional Resources
Nuclear Computational Resource Center (NCRC): https://inl.gov/ncrc/
  Distributes a variety of codes from INL (mostly MOOSE-based)
  More info: https://mooseframework.inl.gov/help/inl/applications.html
The Virtual Test Bed (VTB): https://mooseframework.inl.gov/virtual_test_bed/
  Provides a variety of documented examples of various reactors modeled using MOOSE-based applications